## Slide 1
XOR
AND
1
0
1
A simple, visual look at binary addition — designed & simulated in Logisim
Group : 4
Presented by :
Mallepogu Meghana Sruthi 2620030293
Lakshmi Sahasra Kosuri 2620030254
Yelam Shanmuka Priya 2620030248
Dundigalla Nirmuktha 2620030240
Half Adder & Full Adder

## Slide 2
What Is an Adder?
In digital electronics, computers add binary numbers (0s and 1s) using simple circuits called adders. There are two basic kinds:
HALF ADDER
Adds 2 bits: A and B
Gives 2 outputs: Sum and Carry
Cannot take a carry as input
Used only for the very first bit
S = A ⊕ B C = A · B
FULL ADDER
Adds 3 bits: A, B and Carry-in
Gives 2 outputs: Sum and Carry-out
Can take a carry as input
Used for every other bit position
S = A ⊕ B ⊕ Cin
DDCA | Half Adder & Full Adder
2

## Slide 3
Truth Tables — Every Possible Input
Half Adder
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Full Adder
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Simple rule Sum is 1 when an odd number of inputs are 1. Carry is 1 when 2 or more inputs are 1.
DDCA | Half Adder & Full Adder
3

## Slide 4
Simulating in Logisim
Logisim is a free tool where we drag gates onto a canvas, wire them up, and click inputs to see the outputs light up — no breadboard needed!
1
Place gates
Drag XOR, AND (and OR, for a Full Adder) onto the canvas.
2
Add inputs & outputs
Add Input pins for A, B (and Cin) and Output pins for Sum and Carry.
3
Wire it up
Connect the pins to the gates exactly as in the logic diagram.
4
Click and test
Toggle the input pins between 0 and 1 and check the outputs match the truth table.
DDCA | Half Adder & Full Adder
4

## Slide 5
Key Takeaways
1
A Half Adder adds 2 bits; a Full Adder adds 3 bits (including a carry-in).
2
Both use just a couple of basic gates — XOR, AND, and (for the Full Adder) OR.
3
Logisim lets us build and test these circuits visually before touching real hardware.
4
Full Adders are chained together to build the adders used inside real processors.
DDCA | Half Adder & Full Adder
5

## Slide 6
Simplicity is the ultimate sophistication
- Leonardo da Vinci
Thank You
“
From two gates to a full adder – even the smallest circuits build up to something powerful.